## Slide 1
SANKALP · CLIMATE-SMART AGRICULTURE · WATER · RURAL CREDIT RISK
AquaCast-Punjab
Forecast the aquifer 90 days out — then tell a farmer how many hours to pump, and a bank which loans are about to go bad.
0.099–0.117 m
out-of-sample RMSE 30 / 60 / 90-day forecast
+67.4%
skill vs persistence baseline (Ludhiana)
122
real CGWB wells scored individually, not averaged
84.2%
of rainfall days in the 1,828-day frame are measured telemetry
PyTorch LSTM · 52,547 parameters · 1,828-day daily frame · 3 districts · 122 wells · 8 real Punjab rasters · bilingual English / ਪੰਜਾਬੀ advisory

## Slide 2
THE PROBLEM
Punjab is mining its aquifer — and the paradox hides it
Central Punjab pumps 2,488 MCM of groundwater a year and recharges 2,139 MCM. The 349 MCM gap is the 0.8 m/yr the water table drops — every year, across 280,000 ha of wheat.
The monsoon arrives in July; the water table falls until August.
A 30–40 m deep aquifer lags the monsoon by months — so everyone misreads the signal.
Farmers pump on a calendar, not on a forecast.
Paddy is transplanted in May, before the rain, when the aquifer is at its lowest.
Lenders price crop loans on rainfall, not on water.
Nothing in the credit file says 'this tubewell goes dry in 400 days'.
Recharge peaks in July–August, but the water table is at its deepest exactly then: the monsoon's recharge has not reached 36 m down yet.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
2

## Slide 3
ARCHITECTURE
Four modules, one contract: measured data in, an action out
01
INGEST
3 rain gauges · 5 temp stations 31 CGWB readings · 22 districts
02
RECONSTRUCT
FAO-56 water balance, gamma-lagged recharge, calibrated to the CGWB hydrographs
03
FORECAST
2-layer LSTM, 60-day window, 3 direct horizons (30/60/90 d)
04
ACT
Pumping quota · bilingual WhatsApp/SMS · well-level risk · credit score
Every row of the training frame carries a provenance flag. The dashboard prints the ledger — you can always see which days are measured and which are physics-filled.
Layer | Real or modelled? | Shipped source
Rainfall (daily) | Measured | India-WRIS, 3 gauges
Temperature (daily Tmax/Tmin) | Measured | Punjab SW telemetry, 5 stations
Water level | Measured (sparse) | 31 in-situ CGWB readings, 10 wells
District / block polygons | Real | India-WRIS, 22 Punjab districts
Observation-well network | Real | 122 CGWB wells inside Sangrur
Aquifer thickness, depth to 1st aquifer | Real | CGWB rasters → 440 m grid
Soil texture / depth / slope / erosion | Real | NBSS&LUP rasters
Daily water-level trajectory | Physics + ML | FAO-56 balance, calibrated to the CGWB readings
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
3

## Slide 4
01
Real data, declared provenance
1,828 days · 3 rain gauges · 5 temperature stations · 31 in-situ groundwater readings
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
4

## Slide 5
DATA INTEGRITY
We filled the gaps with physics — and flagged every gap
The WRIS telemetry is real but incomplete: rain gauges report 1,540 of 1,828 days and temperature stations 1,070. Rather than interpolate blindly, we fit a month-specific gamma rainfall model and a 7-term temperature harmonic to the measured record, then generate only the missing days.
84.2% of rainfall days measured
the rest carry rainfall_src = 'generated'
58.5% of temperature days measured
62,339 rows of hourly SW telemetry reduced to daily
Zero silent imputation
every row is auditable in the dashboard's provenance ledger
Closing the balance: 2,488 MCM/yr draft vs 2,139 MCM/yr recharge — a 349 MCM/yr structural deficit, 116% stage of extraction.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
5

## Slide 6
02
The forecast
A PyTorch LSTM that earns its place — and we prove it
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
6

## Slide 7
MODEL
Physics-prior residual learning, on a 60-day window
LSTMs extrapolate linear trends badly.
So the calibrated CGWB depletion rate is subtracted from the target and re-added analytically. The network only models the stationary seasonal residual.
The calendar is a feature, not a nuisance.
sin/cos of day-of-year over the whole window tells the net whether the next 90 days are a Rabi drawdown or a monsoon recovery.
Three districts pooled, one network.
1,713 training sequences instead of 571 — the single biggest win.
Five years of reconstructed water table (blue), the 31 in-situ CGWB readings (red rings), and the live 90-day forecast with its MC-dropout 95% band (amber).
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
7

## Slide 8
OUT-OF-SAMPLE ACCURACY
0.099–0.117 m RMSE at 90 days, 0.935–0.942 R²
District | t+30 | t+60 | t+90 | Overall RMSE | R² | Trend acc. | Skill vs persistence
Sangrur | 0.125 | 0.122 | 0.103 | 0.117 m | 0.935 | 91.7% | +67.4%
Ludhiana | 0.092 | 0.098 | 0.107 | 0.099 m | 0.939 | 90.6% | +70.9%
Moga | 0.121 | 0.115 | 0.106 | 0.114 m | 0.942 | 91.6% | +68.2%
Persistence baseline | — | — | — | 0.341–0.359 m | — | 4.2% | —
Why error FALLS with lead time
The spread of the target grows with horizon (σ 0.21 m → 0.43 m) while the unpredictable part does not. At 30 days the change is driven by individual rain events a 60-day window cannot contain. At 90 days it is driven by the Rabi/monsoon calendar — which is predictable. Per-horizon R² therefore rises 0.65 → 0.94.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
8

## Slide 9
MODEL BAKE-OFF
We trained the boring baselines too. The LSTM still wins.
Model | RMSE (m) | MAE (m) | Trend acc. | Params
LSTM — pooled 3 districts (shipped) | 0.1171 | 0.0919 | 91.7% | 52,547
Linear probe (flatten window) | 0.1427 | 0.1062 | 93.4% | 1,443
GRU (2-layer) | 0.1575 | 0.1257 | 92.8% | 39,363
LSTM — Sangrur only | 0.1584 | 0.1352 | 87.7% | 52,547
Persistence (naive) | 0.3591 | 0.3020 | 4.2% | 0
Identical data, identical split, identical budget. The recurrent model beats the linear probe by 17.9% and a 2-layer GRU by 25.7%.
The honest caveat: the LSTM only wins once the three districts are pooled. Train the identical architecture on Sangrur alone and it scores 0.158 m — worse than the linear probe. Pooling is not a footnote, it is the difference.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
9

## Slide 10
EXPLAINABILITY
Open the black box: what the network actually uses
Four interpretability views, all live
Permutation importance
shuffle each channel, measure the RMSE damage in metres. The calendar carries 72.1%.
Live training curve
train vs validation RMSE, epoch by epoch, from the shipped history.
MC-dropout bands
60 stochastic forward passes — a real epistemic σ, not a ±5% fan chart.
Gradient saliency
input-gradient attribution over the 60-day window.
Read it honestly: doy_sin dominates at 46.0%. That is not a bug — a Punjab aquifer is a seasonal machine, and knowing where you are in the Rabi calendar is most of the forecast. Weather moves the residual.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
10

## Slide 11
ENGINEERING HONESTY
We audited our own evaluation. It was wrong twice.
Stale forecast window
build_sequences stops 90 days short of the record because every training window needs a realised target — so its last row forecast from 90 days BEFORE today. The dashboard's live forecast read -0.01 m. With live_window() it reads -0.43 m, which is what October→December has done in every year of the record.
Trend-prior mismatch
predict() re-adds the depletion prior (rate × horizon), but the ground truth it was scored against did not. That faked a +0.19 m bias and published an RMSE of 0.21 m where the true figure was 0.117 m. R² went 0.789 → 0.935; skill 38.2% → 67.4%.
Both are now regression-tested in tests/smoke_test.py — 24 assertions that fail if either comes back.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
11

## Slide 12
03
The wow features
Four things no other team's prototype will have
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
12

## Slide 13
WOW FEATURE
WOW 01 · The Digital Twin — policy levers in under 0.2 seconds
Six levers, instantly re-solved
Micro-irrigation adoption
0–80%, changes application efficiency
Monsoon anomaly
±30% on monsoon recharge
Paddy transplant shift
0–30 days later, off the pre-monsoon trough
Canal availability
0–100% of the commanded supply
Horizon
90 / 180 / 365 / 730 days
Scenario (365 days) | End level | Water saved
Standard Flood Irrigation | 36.51 m | —
Drip 40% + 15-day paddy shift | 36.37 m | +0.14 m
Micro-Drip Shift (40%) | 36.39 m | +0.12 m
The honest finding: the levers help far less than intuition says. Cut pumping and recharge falls too, because irrigation return flow feeds the aquifer. We surface that instead of hiding it — it is the most policy-relevant thing in the model.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
13

## Slide 14
WOW FEATURE
WOW 02 · One district forecast, 122 individual wells
Block | Mean risk | Wells
ANDANA | 51.5% | 2
MOONAK | 41.9% | 9
SUNAM | 22.7% | 9
SANGRUR | 16.5% | 16
DHURI | 12.5% | 17
BARNALA | 10.8% | 3
Each of the 122 real CGWB wells keeps its own lithology offset, derived from the wells that have in-situ readings and IDW-interpolated to the rest. The district forecast is then applied to every well individually — so ANDANA block sits at 51.5% pump-failure risk while PAKHOWAL sits at 0.0%, in the same district, on the same day. 12 wells are above 50%.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
14

## Slide 15
WOW FEATURE
WOW 03 · The advisory a farmer can actually act on — in Punjabi
WhatsApp · English
*AquaCast Alert — Sangrur*
📅 02 Oct 2026 → 31 Dec 2026 (+90 d)
━━━━━━━━━━━━━━━
💧 Water table: *36.0 → 35.6* m bgl
🔴 Aquifer zone: *OVER-EXPLOITED*
🚰 Pump quota: *1.7 h/week/acre*
(~10 h run, every 40 days)
pump delivery at this depth: 25 m³/h
⚠️ Pump failure risk: *0%*
🌾 Tillering / canopy development
🏦 Loan risk: 62/100 (High)
━━━━━━━━━━━━━━━
⛔ Cut pumping — aquifer below safe threshold.
💧 Shift to drip / sprinkler to cut draft 40%.
WhatsApp · ਪੰਜਾਬੀ
*ਐਕੁਆਕਾਸਟ ਚੇਤਾਵਨੀ — Sangrur*
📅 02 ਅਕਤੂ 2026 → 31 ਦਸੰ 2026 (+90 ਦਿਨ)
━━━━━━━━━━━━━━━
💧 ਪਾਣੀ ਦਾ ਪੱਧਰ: *36.0 → 35.6* ਮੀਟਰ ਹੇਠਾਂ
🔴 ਧਰਤੀ ਹੇਠਲੇ ਪਾਣੀ ਦੀ ਹਾਲਤ: *ਵੱਧ-ਖਿੱਚ*
🚰 ਟਿਊਬਵੈੱਲ ਸਮਾਂ: *1.7 ਘੰਟੇ / ਹਫ਼ਤਾ / ਏਕੜ*
(~10 ਘੰਟੇ, ਹਰ 40 ਦਿਨਾਂ ਬਾਅਦ)
ਇਸ ਡੂੰਘਾਈ ਤੇ ਪੰਪ ਡਿਲੀਵਰੀ: 25 ਮੀ³/ਘੰਟਾ
⚠️ ਪੰਪ ਖ਼ਰਾਬ ਹੋਣ ਦਾ ਖ਼ਤਰਾ: *0%*
🌾 ਕੱਲੀਆਂ ਨਿਕਲਣਾ
🏦 ਕਰਜ਼ੇ ਦਾ ਖ਼ਤਰਾ: 62/100 (ਉੱਚਾ)
━━━━━━━━━━━━━━━
⛔ ਪੰਪਿੰਗ ਘਟਾਓ — ਪਾਣੀ ਸੁਰੱਖਿਅਤ ਪੱਧਰ ਤੋਂ ਹੇਠਾਂ ਹੈ।
💧 ਤੁਪਕਾ / ਛਿੜਕਾਅ ਸਿੰਚਾਈ ਅਪਣਾਓ।
Also shipped
SMS fallback
160-char version for feature phones
HTML → PDF
printable district advisory
CSV / JSON export
for the bank's own pipeline
The quota is in farmer units, not mm/week. "Run the pump 10 hours, then wait 40 days." Discharge is derated to the head the pump actually works against (25 m³/h at 35.6 m — not the free-delivery nameplate). Deeper water means more hours and more power for the same crop.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
15

## Slide 16
WOW FEATURE
WOW 04 · The Model Lab — we show you the receipts
Live training curve
Train vs validation RMSE, epoch by epoch, read from the shipped checkpoint. Not a screenshot — the actual history object.
MC-dropout bands
60 stochastic forward passes at inference. The ±σ you see is real model uncertainty, not a decorative fan.
Permutation importance
Shuffle a channel, re-score, report the damage in metres. Repeats give you the error bar.
Gradient saliency
Input-gradient attribution across the 60-day window — which days moved the forecast.
Model benchmark
LSTM vs GRU vs linear probe vs persistence, retrained live in the app on identical data.
Provenance ledger
Measured vs generated days, station counts, file names — printed on the same screen as the metrics.
Why it wins rooms: a judge can click a button and watch the model train, explain itself, and lose to a linear probe on purpose. That is harder to fake than a metric.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
16

## Slide 17
CREDIT RISK
The same forecast, priced: who defaults when the well goes dry
District | Risk score | Band | PD | Exposure | Expected loss
Sangrur | 62/100 | High | 9.40% | ₹191 cr | ₹10.8 cr
Ludhiana | 33/100 | Moderate | 3.27% | ₹294 cr | ₹5.8 cr
Moga | 37/100 | Moderate | 3.91% | ₹121 cr | ₹2.8 cr
₹607 cr
portfolio exposure
3.2%
portfolio-at-risk
₹19.4 cr
expected loss
₹4.3 cr
avoidable with advisory
Seven weighted drivers — depth, pump-failure risk, forecast drawdown, stage of extraction, crop stage, monsoon anomaly and drip adoption — produce a 0–100 score, a probability of default and a rupee expected loss. The bank gets a number it can price; the farmer gets an early-warning text, not a rejection.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
17

## Slide 18
HOW IT IS BUILT
Production engineering, not a notebook
One command, whole system
python3 run_pipeline.py — pre-flight, ingest, build, train, evaluate, advise, launch. 45 s cold.
24 automated assertions
3 districts × (advisory, wells, twin, spatial, geojson) + evaluation, importance, saliency, every chart, and the two audit regressions.
Caching everywhere
Climate model, datasets, forecasts and maps are content-hashed and cached — the UI never waits on a fit.
No mocked numbers
Every figure in the app and this deck is computed from data/ at run time. Change the data, the deck rebuilds itself.
Typed, documented, linted
Docstrings carry the physical reasoning, not just the signature. Constants are named and collected in one config module.
Graceful degradation
No model checkpoint? The app still serves the physics twin and the advisory. No map? It falls back to a scatter.
Reproducible
Seeded torch/numpy, pinned requirements.txt, a rebuild script for the spatial assets, and an artefacts manifest on exit.
Honest by construction
Baselines ship with the model. Provenance columns ship with the data. Limitations ship with the README.
52,547 parameters · 1,828-day daily frame · 1,713 training sequences · ~25 s to train on CPU · sub-0.2 s digital twin · 4-tab Streamlit dashboard · 26 MB of real Punjab data
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
18

## Slide 19
LIMITATIONS
What we would tell a reviewer before they ask
The daily trajectory is modelled, not measured.
Only 31 in-situ CGWB readings exist for these districts (2021–2024). The continuous daily curve is a calibrated FAO-56 water balance. We anchor its level to the readings and its decline to the published district rate — but it is a reconstruction, and the RMSE figures measure forecast skill against that reconstruction.
31 readings is a thin calibration set.
The recharge lag and scalar are fitted to them. More well data would tighten both. The seasonal-shape fit is 0.47–0.50 m after removing each well's static lithology offset.
Part of the weather record is generated, not measured.
84.2% of rainfall days and 58.5% of temperature days are measured telemetry; the gaps — scattered through the record, and every day after the gauges stop reporting — come from the fitted climate model. Every row is flagged, and both are visible in the chart above.
Three districts, not 23.
Sangrur, Ludhiana and Moga were chosen because the Drive data covers them. The spatial layer ships all 22 Punjab districts, so extension is a data-refresh, not a rewrite.
None of these are hidden in the product: the dashboard's provenance tab prints all of them.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
19

## Slide 20
IMPACT
Why this wins
A forecast that beats the obvious baselines, and we prove it
0.099–0.117 m RMSE, 67.4–70.9% skill vs persistence, reported next to persistence, seasonal-naive, linear-trend, a GRU and a linear probe.
Real Punjab data, and an honest account of every gap
1,828-day frame, 1,540 measured rainfall days, 31 CGWB readings, 122 wells, 8 real rasters.
It ends in an action, not a chart
A pumping quota in hours-per-irrigation, a bilingual WhatsApp card, a well-level risk map and a credit score.
You can open it and check
Live training curve, MC-dropout bands, permutation importance, gradient saliency, a re-trainable benchmark, and a provenance ledger.
Next 90 days
Extend to all 22 Punjab districts
spatial layer already ships them
Ingest CGWB's quarterly well census automatically
replaces the static reading set
Pilot with a regional rural bank
portfolio view is already priced in ₹
Add a farmer reply loop (STOP / CONFIRM)
the SMS contract is already written
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
20

## Slide 21
THE PRODUCT
One model, three rooms
The same forecast means three different things to three different people. One switcher, three views, one model underneath.
📱 Kisan mobile
375 px, high contrast
one dial, one instruction
English / ਪੰਜਾਬੀ
Gurmukhi toggle, not transliteration
Safe · Warning · Pump failure
from the advisory's own zone
“Run the pump 6 h, 22:00–04:00”
a window, not a warning
Next critical stage in 30 d
CRI and flowering cannot be missed
WhatsApp / SMS push
with a Gurmukhi fallback
🧑‍🌾 Farmer desktop
Water budget, season by season
Rabi / Zaid / Kharif in MCM
Neighbour-pump calculator
Cooper–Jacob at your spacing
Rotation simulator
shift hectares out of paddy
Drilling calculator
₹ by depth, HP and pump class
Strata cross-section
where the table is going, in m and ₹
🏛️ Administrator & Finserv
Wells, lithology, dependency arcs
click a well, see its cone
Block stress heatmap
real blocks, real wells
Portfolio at risk in ₹ Crore
over-exploited vs critical
Deepening vs drip NPV
which one do we finance?
8-hour supply optimiser
rotate feeders against crop stage
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
21

## Slide 22
MODULES A & B
The physics: nobody's pump is the problem, everybody's is
0.046 m
one tubewell moves a neighbour's piezometer
690 bores · 15 village clusters
0.96 m
the same village, superposed
a 0.8% sample of 92,000 real bores
59%
of the year's draft pumped before wheat sowing
1,468 MCM, 1 Jun → 1 Nov
0.85 m
annual swing, on top of 0.65 m/yr
deepest Jul · shallowest Dec
Full-year rotation, priced
Rabi wheat
350 mm → 980 MCM
Kharif paddy
550 mm → 1,441 MCM, ponded
Zaid summer
70 MCM on a minority of holdings
Reconciles with the twin
2,491 MCM/yr vs its 2,488
We checked the brief against the data
“Monsoon flooding depletes the aquifer before November sowing.” — it does not.The detrended hydrograph bottoms out in Jul and peaks in Dec. The monsoon refills the aquifer; the Rabi wheat season drains it into the summer trough. The monsoon refills but does not restore — each November starts 0.65 m deeper than the last.
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
22

## Slide 23
MODULE C
The ground: 8.0 m from the next aquifer, 10.0 years away
Sangrur is pumping from L1 today. At 0.8 m/yr it crosses into L2 around 2036 — and the step is not free.
Unit | Depth | Pump | Duty | Bore cost
L1 Shallow unconfined | 0–40 m | Submersible | 8.6 HP | —
L2 Semi-confined | 40–90 m | Submersible | 15.3 HP | +₹1.36 L
L3 Deep confined | > 90 m | High-head submersible | 25–40 HP | +₹1.6 L more
Measured, not assumed — 25 real CGWB lithologs in Sangrur:median transmissivity 1,620 m²/d · median drilled depth 210 m · median EC 733 µS/cm · 0.0% above the saline threshold.We do not claim the deep water is saltier. EC correlates with drilled depth at r = +0.024 — no relationship. Salinity is flagged as a literature risk, never as a finding.
Why deepening compounds
The pump must change
8.6 → 15.3 HP
The bore must be cased deeper
casing dominates the bill
And it is a depleting asset
you buy N years, then repeat
Real bores already go deep
median 210 m in the logs
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
23

## Slide 24
MODULES D & F
The money: what should the lender actually finance?
21.2 yr
until the existing bore stops delivering
at 0.8 m/yr
₹1.1 L
drip on the existing grid connection
payback 3.7 yr · NPV ₹119,471
₹2.1 L
deepening the bore instead
payback 22.9 yr · NPV ₹-82,315
269×
finer than a GRACE cell, linearly
384 m inputs vs 10,677 km²
Verdict: Drip Only
Deepening is not wrong, it is just badly timed. It costs ₹213,348 and its benefit does not begin until year 21.2 — after which it buys 28.8 years, and then you repeat.Drip pays from year one, and cut the draft that causes the decline: +13.0 years of bore life on the existing pump.The solar pump is the worst of the three (NPV ₹-206,029) — not because solar is bad, but because Punjab's farm power is subsidised to ~zero, so it displaces electricity nobody was paying for.
System | Resolution | Lead time | Ends in an action?
NASA GRACE | ~10,677 km²/cell | None — retrospective | No
CGWB India-WRIS | point wells, 4×/yr | None — 6–12 mo lag | No
PAU tensiometer | one field | Same day | Irrigate now
AquaCast | 384 m inputs | 30 / 60 / 90 days | Yes — hours & ₹
AquaCast-Punjab · Sankalp — Climate-Smart Agriculture, Water & Rural Credit
24

## Slide 25
THE ONE-LINER
Every other team will show you a groundwater chart. We show a farmer which hours to pump, and a bank which loan is about to go dry.
0.099–0.117 m RMSE · up to +70.9% skill · 3 districts · 122 wells scored · 1,828-day frame · bilingual · 52,547-parameter PyTorch LSTM
Run it: python3 run_pipeline.py → dashboard on :8501 · Verify it: python3 tests/smoke_test.py → 25 passed